Technical Safety Concept Lane Assistance
Document Version: [Version]
Template Version 1.0, Released on 2017-06-21

# Document history

Date	Version	Editor	Description
26/05/18	1	Shaikh Mohammed Shadab	First attempt

# Table of Contents

# Purpose of the Technical Safety Concept

The technical safety concept shall expand upon the functional safety requirements, detailing
how each of them shall be realized, through various components and sub-systems present in
the system. Further, the technical concepts describe what a system shall do when a malfunction
violates the safety goal.
# Inputs to the Technical Safety Concept
## Functional Safety Requirements

ID	Functional Safety Requirement	ASIL	Fault Tolerant Time Interval	Safe State
Functional / Safety / Requirement / 01-01	The lane keeping item shall ensure that the lane departure oscillating torque amplitude is below Max_Torque_Amplitude	C	50ms	LDW feature should be turned off
Functional / Safety / Requirement / 01-02	The lane keeping item shall ensure that the lane departure oscillating torque frequency is below Max_Torque_Frequency	C	50ms	LDW feature should be turned off
Functional / Safety / Requirement / 02-01	The electronic power steering ECU shall ensure that the lane keeping assistance torque is applied for only Max_Duration	B	500 ms	LKA system should be turned off

## Refined System Architecture from Functional Safety Concept

### Functional overview of architecture elements

Element	Description
Camera Sensor	The camera sensor just reads in images from the road
Camera Sensor ECU - Lane Sensing	This units is computer vision system to detect lane lines
Camera Sensor ECU - Torque request generator	Generated request for torque for LDW warning
Car Display	This is the display unit where all relevant data is displayed
Car Display ECU - Lane Assistance On/Off Status	Check whether Lane assisstance system is on
Car Display ECU - Lane Assistant Active/Inactive	Check whether Lane Assisstance system is on or off
Car Display ECU - Lane Assistance malfunction warning	Check whether Lane Assisstance system is gives warning for unintentional lane change
Driver Steering Torque Sensor	This units checks the torque applied on steering wheel by the driver
Electronic Power Steering (EPS) ECU - Driver Steering Torque	Sends signal for generating torque which is restricted to a maximum limit max_torque
EPS ECU - Normal Lane Assistance Functionality	Generates oscilatory torque for alerting the driving
EPS ECU - Lane Departure Warning Safety Functionality	Check if torque to steering wheel is within limits and it is not in limit warning signal is indicated
EPS ECU - Lane Keeping Assistant Safety Functionality	Check whether LKA system applies torque for fixed duration of time
EPS ECU - Final Torque	Provide torque signal to steering after all safety checks
Motor	This the actuator which applies the torque.

# Technical Safety Concept

## Technical Safety Requirements
Lane Departure Warning (LDW) Requirements:

Functional Safety Requirement 01-01 with its associated system elements
(derived in the functional safety concept)
ID	Functional Safety Requirement	Electronic Power Steering ECU	Camera ECU	Car Display ECU
Functional / Safety / Requirement / 01-01	The lane keeping item shall ensure that the lane departure oscillating torque amplitude is below Max_Torque_Amplitude	X

Technical Safety Requirements related to Functional Safety Requirement 01-01 are:
ID	Technical Safety Requirement	ASIL	Fault Tolerant Time Interval	Architecture Allocation	Safe State
Technical / Safety / Requirement / 01	The LDW safety component shall ensure that the amplitude of the 'LDW_Torque_Request' sent to the 'Final electronic power steering Torque' component is below 'Max_Torque_Amplitude.	C	50ms	LDW safety block	Set LDW_torque_amplitude to zero
Technical / Safety / Requirement / 02	As soon as the LDW function deactivates the LDW feature, the 'LDW Safety' software block shall send a signal to the car display ECU to turn on a warning light.	C	50ms	Data Transmission Integrity Block	Lane Assistance System in turned if Data_validity is False
Technical / Safety / Requirement / 03	As soon as a failure is detected by the LDW function, it shall deactivate the LDW feature and the 'LDW_Torque_Request' shall be set to zero.	C	50ms	LDW safety block	Lane Assistance System is turned off
Technical / Safety / Requirement / 04	The validity and integrity of the data transmission for 'LDW_Torque_Request' signal shall be ensured.	C	50ms	LA Malfunction Warning Block	Lane Assistance System is turned off with Error_status True
Technical / Safety / Requirement / 05	Memory test shall be conducted at start up of the EPS ECU to check for any faults in memory.	A	50ms	Memory Test Block	Lane Assistance System is turned off

Functional Safety Requirement 01-2 with its associated system elements
(derived in the functional safety concept)
ID	Functional Safety Requirement	Electronic Power Steering ECU	Camera ECU	Car Display ECU
Functional / Safety / Requirement / 01-02	The lane keeping item shall ensure that the lane departure oscillating torque frequency is below Max_Torque_Frequency	X

Technical Safety Requirements related to Functional Safety Requirement 01-02 are:
ID	Technical Safety Requirement	ASIL	Fault Tolerant Time Interval	Architecture Allocation	Safe State
Technical / Safety / Requirement / 01	The LDW safety / component shall ensure / that the amplitude of / the / ‘LDW_Torque_Request’ / sent to the ‘Final EPS / Torque’ component is / below / Max_Torque_Amplitude	C	50ms	LDW safety block	Set LDW_torque_amplitude to zero
Technical / Safety / Requirement / 02	The validity and / integrity of the / LDW_Torque_Request / signal shall be ensured	C	50ms	Data Transmission Integrity Block	Lane Assistance System in turned if Data_validity is False
Technical / Safety / Requirement / 03	As soon as failure is / detected by the LDW / function, the / LDW_Torque_Request / shall be set to zero	C	50ms	LDW safety block	Lane Assistance System is turned off
Technical / Safety / Requirement / 04	As soon as the LDW / function deactivates the / LDW feature, the / software block shall / send a signal to turn on / a warning light	C	50ms	LA Malfunction Warning Block	Lane Assistance System is turned off with Error_status True
Technical / Safety / Requirement / 05	Memory tests shall be / conducted at the start / of EPS ECU to check / for any faults in memory	A	50ms	Memory Test Block	Lane Assistance System is turned off

Lane Keeping Assistance (LKA) Requirements:

Functional Safety Requirement 02-1 with its associated system elements
(derived in the functional safety concept)

ID	Functional Safety Requirement	Electronic Power Steering ECU	Camera ECU	Car Display ECU
Functional / Safety / Requirement / 02-01	The lane keeping item shall ensure that the lane keeping assistance torque is applied for only Max_Duration	X

Technical Safety Requirements related to Functional Safety Requirement 02-01 are:
ID	Technical Safety Requirement	ASIL	Fault Tolerant Time Interval	Allocation to Architecture	Safe State
Technical / Safety / Requirement / 01	The LKA system shall stop sending LKA_Torque_Request once Max_Duration is completed	B	500ms	LKA safety block	Shut down LKA system, as duration> Max_duration
Technical / Safety / Requirement / 02	The validity and integrity of the LKA_Torque_Request signal shall be ensured	B	500ms	Data transmission Integrity block	Lane Assistance System is turned if Data_validity is False
Technical / Safety / Requirement / 03	As soon as failure is detected by the LKA function, the LKA_Torque_Request shall be set to zero	B	500ms	LKA safety block	Lane Assistance System is turned off
Technical / Safety / Requirement / 04	As soon as the LKA function deactivates the LKA feature, the software block shall send a signal to turn on a warning light	B	500ms	LA malfunction warning block	Lane Assistance System is turned off with Error_status_true
Technical / Safety / Requirement / 05	Memory tests shall be conducted at the start of EPS ECU to check for any faults in memory	A	Length of ignition cycle	Memory test block	Lane Assistance System in turned off

## Refinement of the System Architecture

## Allocation of Technical Safety Requirements to Architecture Elements

All technical safety requirements are allocated to EPS ECU.
## Warning and Degradation Concept

ID	Degradation Mode	Trigger for Degradation Mode	Safe State invoked?	Driver Warning
WDC-01	Shut down	Malfunction_01 / Malfunction_02	Yes	Indicator on Car display showing max torque/frequency
WDC-02	Shut down	Malfunction_03	Yes	Indictor on Car display turn off when LKA turned off